# Solutions to Quiz #1

# Question 1

## An acre is equal to 160 square rods, where 1 rod = 5.5 yards and 1 yard = 0.914 meters.  How many square meters are there in an acre?

# Question 2a (5 points)

## A particle undergoes four displacements as follows:  A = 80 m along pos. x; B = 60 m at 30o above x; C = 40 m at 45o above -x; D = 100 m at 60o below -x.  Graphical Solution

# Question 2b (5 points)

## A particle undergoes four displacements as follows:  A = 80 m along pos. x; B = 60 m at 30o above x; C = 40 m at 45o above -x; D = 100 m at 60o below -x.  Component Solution

# Question 3 (6 points)

## If a force of 86 N parallel to the surface of a 20o inclined plane will push a 120 N block up the plane at constant speed, what force parallel to the plane will push it down at constant speed?  What is coefficient of kinetic friction?

# Text boxes

1

1

1

1

1

1

1

1

(

(

(

(

R = 60 m

at 27o below x

R

D

C

B

A

1

1

1

(

(

### 86 N

20o

Ff

120N(cos20)

#### N

120N(sin20)

86 N

### 120 N