## Slide 1
Transport-Specific Programming David Treadwell Jameel Hyder Software Design Engineers Windows NT Networking Microsoft Corporation

## Slide 2
TCP/IP And Winsock
Traditional transport protocol under Winsock
Protocols supported
  TCP: reliable and stream-oriented
  UDP: unreliable datagrams

## Slide 3
TCP/IP Name Resolution
Works with both getXbyY() and RNR APIs
Name resolution mechanisms
  Local cache and host name
  Hosts file
  DNS
  WINS/NetBIOS broadcast

## Slide 4
TCP/IP Performance Issues
Nagling: coalesces sends
  Useful for reducing network traffic
  Big performance hit for applications which do small sends
  Disable with TCP_NODELAY sockopt
TCP PUSH bit
  Set on last packet of a send buffer
  Holds on to receive buffers for 0.5 sec
Code example: slides 4a, 4b

## Slide 5
TCP/IP Multicast: IGMP
Supported in Windows NT™ 3.5 and Windows® 95
Uses same interface as BSD UNIX
Sending multicasts
  Simply send to multicast address
Receiving multicasts
  Use IP_ADD_MEMBERSHIP socket option
Code example: slides 5a, 5b

## Slide 6
IPX/SPX And Winsock
Supported in both Windows NT and Windows 95
Protocols supported are:
  SPX: reliable, message or stream- oriented
  IPX: unreliable datagrams
See wsipx.h and wsnwlink.h header files

## Slide 7
IPX/SPX Name Resolution
Does not work with getXbyY() calls
Supported with RNR APIs
Use GetAddressByName() with
  Name space = NS_SAP
  GUID containing SAP ID
  See svcguid.h header file

## Slide 8
SPX Messages
SPX uses “EOM” bit
Respected on receive with SOCK_SEQPACKET sockets
Ignored with SOCK_STREAM
WSARecvEx() API

## Slide 9
Special IPX/SPX Sockopts
Various extension sockopts for special needs
  See wsnwlink.h for details
Receive full IPX/SPX header
Get local address with getsockname() API
Disable broadcast reception
Set/get IPX packet type

## Slide 10
NetBIOS And Winsock
Useful for compatibility with old applications
  Allows use of a single transport API
Not suggested for new application protocols
Works with any protocol that supports NetBIOS semantics:
  NetBEUI
  NBT: NetBIOS over TCP/IP (RFC 1001/1002)
  NetBIOS over IPX

## Slide 11
Supports only SOCK_SEQPACKET and SOCK_DGRAM
Supported only in Windows NT
Name resolution is implicit in NetBIOS
See wsnetbs.h header file
NetBIOS And Winsock

## Slide 12
Opening NetBIOS Sockets
Each exported NetBIOS protocol has a Lana number
The “protocol” parameter of socket() API is -1 * Lana
Clients should loop opening sockets and attempting connect()
Servers should listen() on all Lanas
Code example: slide 12

## Slide 13
AppleTalk® And Winsock
Protocols supported
  DDP: unreliable datagrams
  PAP: reliable and message- oriented only
  ADSP: reliable and message or stream-oriented
Name lookup/registration (NBP)
Zone lookup/browsing (ZIP)

## Slide 14
AppleTalk Address Structure
typedef struct sockaddr_at
{
USHORT sat_family;
USHORT sat_net;
UCHAR sat_node;
UCHAR sat_socket;
} SOCKADDR_AT, *PSOCKADDR_AT;

## Slide 15
Name Resolution/Lookup (NBP)
Handled via getsockopt/setsockopt
Name registration/deregistration
  SO_REGISTER_NAME
  SO_DEREGISTER_NAME
Browsing
  SO_LOOKUP_NAME
  SO_CONFIRM_NAME
Does not work with RnR

## Slide 16
Browsing Zones (ZIP)
Handled via getsockopt
  Configuration
    SO_GETMYZONE
  Browsing
    SO_GETZONELIST (for entire appletalk internet)
    SO_GETLOCALZONES (for a specific network)
Does not work with RnR

## Slide 17
Protocol Details
DDP Protocol
  Supports SOCK_DRAM only
  Can use both dynamic as well as static sockets
ADSP Protocol
  Supports both SOCK_RDM and SOCK_STREAM

## Slide 18
PAP Protocol
  Only supports SOCK_RDM
  Non blocking recieves handled via setsockopt(SO_PAPPRIMEREAD)
  getsockopt/setsockopt used for PAP status messages
Protocol Details